## Slide 1
GridTrace AI
Finding energy loss — and knowing when not to blame anyone
Hybrid Isolation Forest + autoencoder anomaly detection with hierarchical localization and explainable investigation scoring.
16.16%
India's AT&C losses, FY25
92.2%
normal data correctly left alone
93%
network events not blamed on a consumer
Nirmal (Muthukumar R) · Team Squad Mavericks · Sustainable Energy & Resource Innovation
Notes: GridTrace AI. The one line to remember: this system is as careful about who it does NOT accuse as about what it detects.

## Slide 2
THE PROBLEM
Electricity is delivered. Some of it is never accounted for.
16.16%
of energy entering India's distribution network is lost as Aggregate Technical & Commercial (AT&C) loss — FY25, Ministry of Power.
Every unit lost is billed to somebody: honest consumers through tariffs, or the state through subsidy.
1
Technical loss
Resistive heating in lines and transformers. Physics. Always present, roughly 3%.
2
Faulty metering
A meter that drifts or under-registers looks identical to loss in the billing data.
3
Metering / data gaps
A meter offline for a week produces a hole that looks exactly like theft.
4
Unmetered consumption
Genuine unbilled draw — the case utilities actually want to find.
Four different causes. One identical signature in the data.
Source: Ministry of Power / PFC, FY2024-25 distribution utility performance.
Notes: Set up the central difficulty: the four causes are indistinguishable in raw billing data. That is why a detector alone is not enough.

## Slide 3
PROBLEM DEPTH
The money has been spent. The losses stopped falling.
Chart: AT&C losses, % of energy input
| FY 2021 | 2023 | FY 2025
AT&C losses | 21.91 | 15.5 | 16.16
₹2.83 lakh crore
sanctioned under RDSS, ₹1.53 lakh crore of it for distribution infrastructure.
Losses fell 21.91% → 15.5% on infrastructure alone, then stalled and ticked back up. The remaining loss is not the kind you fix with more hardware.
▪
It is unattributed — the gap is visible at the feeder, invisible per meter.
▪
Inspection is manual, slow, and guided by suspicion rather than evidence.
▪
A wrong accusation costs a utility more than the unit it recovers.
RDSS target: 12–15% national AT&C losses. Sources: Ministry of Power, PFC discom performance report.
Notes: The plateau is the whole argument. Capital fixed the easy losses; what is left needs attribution, not more copper.

## Slide 4
EXISTING SOLUTIONS
What is deployed today, and where each one stops.
1
Smart meters / AMI
Measures beautifully. Reports consumption, not causation — the gap still has to be explained by a human.
Measurement only
2
Threshold alarms
"Flag if usage drops 40%." Fixed rules fire on holidays and seasonal shifts; teams learn to ignore them.
High false-positive rate
3
Manual inspection drives
Effective but expensive, and targeted by intuition or complaint rather than by evidence.
Does not scale
4
Single-model ML research
Strong published accuracy on one detector, evaluated offline. Rarely localizes, rarely explains, rarely deployed.
Detection ≠ action
The market has detection. What it lacks is a defensible answer to "so where do I send the inspector, and why?"
Notes: Be fair to existing tools — they work at what they do. The gap is between an alarm and an action.

## Slide 5
GAP & INNOVATION
The innovation is the chain, not any single link.
We claim no novelty in Isolation Forests, autoencoders, energy-balance auditing or explainable AI. Each is established. What does not exist as one working pipeline is this:
Detect
→
Classify
cause
→
Correlate
network +
consumer
→
Localize
hierarchically
→
Score with
explanation
→
Prioritise
investigation
1
Two models, one verdict
Isolation Forest and the autoencoder fail differently. Calibrated to a common scale, agreement between them becomes evidence rather than noise.
2
It knows when to say nobody
A feeder gap no meter explains is reported as unattributed loss at the feeder — not pinned on the highest scorer.
3
Every score is defensible
Reasons come from the values that produced the score, so an inspector can check the reasoning before knocking on a door.
Positioning: integration and workflow are the contribution; the underlying techniques are deliberately proven ones.
Notes: Say the honesty line out loud — judges reward a team that knows exactly what it did and did not invent.

## Slide 6
SOLUTION ARCHITECTURE
Runs end to end on one laptop. No cloud.
1
ESP32 / Wokwi
5 meters, 2 zones,
1 feeder
→
2
MQTT
local broker,
180 lines of Python
→
3
Collector
validate; malformed
messages dropped
→
4
Feature engine
9 consumer-relative
features, streaming
5
Hybrid AI
Isolation Forest
+ autoencoder
→
6
Risk score
0–100, four
investigation bands
→
7
Localization
Network → Feeder
→ Zone → Consumer
→
8
Store + dashboard
SQLite (WAL),
Flask, MQTT alert
numpy · scikit-learn · paho-mqtt · flask
5 dependencies
no TensorFlow, no Mosquitto, no Docker
nothing to install
~10 s to train, <1 s per frame to score
laptop-grade
Notes: Emphasise that the whole thing is running now, locally, and can be demonstrated in one command.

## Slide 7
AI · LOCALIZATION · EXPLAINABILITY
How two models become one defensible number.
1
Calibrate
Raw scores live on incompatible scales. Each is converted to its percentile within known-normal data.
2
Severity
severity = −log₁₀(1−p) / 3. Each extra "nine" of rarity adds fixed risk, so median-normal scores 0.10, not 0.50.
3
Combine
hybrid = 0.5·mean + 0.5·max. Mean rewards agreement; max keeps what only one model can see.
4
Risk 0–100
100·hybrid + 12·network evidence + 12·persistence. Evidence terms capped so imbalance alone can never convict.
Chart: Feeder gap by scenario, % (measured)
| Normal | Abnormal | Persistent | Imbalance
Instantaneous unaccounted power | 3.1 | 4.4 | 8.25 | 13.79
Localization rule
If the feeder gap exceeds its technical-loss floor AND no consumer scores ≥ 61 — report FEEDER, unattributed. Fires on 93% of network-event frames.
Output says "high-risk anomaly — investigation required". Never "theft proven".
Notes: The severity transform is the detail worth naming — it is why normal data does not sit at 50/100.

## Slide 8
FEASIBILITY & SCALABILITY
Already built, already measured.
10
checks passing
end to end
1,120
messages, zero
loss on the wire
92.2%
normal readings
left alone
~10 s
full retrain on
a laptop
Validated behaviour
✓
Normal telemetry: 92.2% NORMAL band, 0.1% high-risk — usable false-positive rate.
✓
Injected anomalies: flagged consumers match the ground-truth field the models never see.
✓
Network-only events: localized to the feeder, no consumer accused, in 93% of frames.
✓
Malformed and NaN telemetry rejected without interrupting the stream.
Path to scale
One model, not one per meter
Features are consumer-relative, so the same trained model generalises from 5 meters to 50,000.
Transport already standard
MQTT is what AMI head-ends speak. Swap the simulator for a serial or head-end feed; nothing downstream changes.
Cost of being wrong is bounded
Capped evidence terms and the unattributed rule keep false accusations structurally unlikely.
All figures measured by tests/test_pipeline.py on the working prototype, not projected.
Notes: Every number here is reproducible in front of the judges in about two minutes.

## Slide 9
MARKET IMPACT & FUTURE
Recover the loss without manufacturing suspicion.
1 point
of AT&C loss recovered is worth thousands of crores annually across India's discoms.
12–15%
is the national RDSS target. Attribution — not more hardware — is what closes the last gap.
Every utility
with AMI already produces the telemetry this needs. No new sensing required.
Where it goes next
▸
Real AMI feed in place of the simulator — the MQTT contract is unchanged.
▸
Cause classification as a supervised layer once inspection outcomes exist as labels.
▸
Inspection prioritisation queue: rank by risk × recoverable energy × access cost.
▸
Feeder-segment localization below the zone, once sub-metering is available.
The line we will not cross
This system produces an investigation priority, never a verdict. An energy gap has four honest explanations, and a tool that forgets that turns statistical noise into an accusation against a real household.
GridTrace AI · Team Squad Mavericks
Notes: Close on the restraint. It is the most defensible thing about the project and the hardest thing for a competing team to retrofit.